## Slide 1: Device Tree Introduction

## Slide 2: Reference
Wiki – Device Tree Usage http://devicetree.org/Device_Tree_Usage
ePAPR Version 1.1 https://www.power.org/wp-content/uploads/2012/07/Power_ePAPR_APPROVED_v1.1.pdf
Experiences with device tree support development for ARM based SoC's http://elinux.org/images/4/48/Experiences_With_Device_Tree_Support_Development_For_ARM-Based_SOC%27s.pdf
Device Trees http://elinux.org/Device_Trees
U-BOOT cmd fdt http://www.denx.de/wiki/view/DULG/UBootCmdFDT

## Slide 3: What is Device Tree
The Device Tree is a data structure for describing hardware. Rather than hard coding every detail of a device into an operating system, many aspect of the hardware can be described in a data structure that is passed to the operating system at boot time. The device tree is used both by Open Firmware, and in the standalone Flattened Device Tree (FDT) form.
The data structure itself is a simple tree of named nodes and properties. Nodes contain properties and child nodes. Properties are simple name-value pairs. The structure can hold any kind of data.
However, in order to be useful, device tree data must be laid out in a structure that operating systems can understand. A "bindings" is a description of how a device is described in the device tree. Bindings for a lot of devices are well established and documented.

## Slide 4: History (1)
The DT was originally created by Open Firmware as part of the communication method for passing data from Open Firmware to a client program (like to an operating system). An operating system used the Device Tree to discover the topology of the hardware at runtime, and thereby support a majority of available hardware without hard coded information (assuming drivers were available for all devices).
Since Open Firmware is commonly used on PowerPC and SPARC platforms, the Linux support for those architectures has for a long time used the Device Tree.

## Slide 5: History (2)
In 2005, when PowerPC Linux began a major cleanup and to merge 32-bit and 64-bit support, the decision was made to require DT support on all powerpc platforms, regardless of whether or not they used Open Firmware. To do this, a DT representation called the Flattened Device Tree (FDT) was created which could be passed to the kernel as a binary blob without requiring a real Open Firmware implementation. U-Boot, kexec, and other bootloaders were modified to support both passing a Device Tree Binary (dtb) and to modify a dtb at boot time.
Some time later, FDT infrastructure was generalized to be usable by all architectures. At the time of this writing, 6 mainlined architectures (arm, microblaze, mips, powerpc, sparc, and x86) and 1 out of mainline (nios) have some level of DT support.

## Slide 6: High Level View
Using it allows board and device support to become data driven; to make setup decisions based on data passed into the kernel instead of on per-machine hard coded selections.
Ideally, data driven platform setup should result in less code duplication and make it easier to support a wide range of hardware with a single kernel image. Linux uses DT data for three major purposes:
  platform identification
  runtime configuration
  device population

## Slide 7: Basic Data Format
/ {
node1 {
a-string-property = "A string";
a-string-list-property = "first string", "second string";
a-byte-data-property = [0x01 0x23 0x34 0x56];
child-node1 {
first-child-property;
second-child-property = <1>;
a-string-property = "Hello, world";
};
child-node2 {
};
};
node2 {
an-empty-property;
a-cell-property = <1 2 3 4>; /* each number (cell) is a uint32 */
child-node1 {
};
};
};

## Slide 8: CPU addressing
/ {
cpus {
#address-cells = <1>;
#size-cells = <0>;
cpu@0 {
compatible = "arm,cortex-a9";
reg = <0>;
};
cpu@1 {
compatible = "arm,cortex-a9";
reg = <1>;
};
};
...
}

## Slide 9: Memory Mapped Devices (on SoC)
/ {
#address-cells = <1>;
#size-cells = <1>;
...
serial@101f0000 {
compatible = "arm,pl011";
reg = <0x101f0000 0x1000>;
};
gpio@101f3000 {
compatible = "arm,pl061";
reg = <0x101f3000 0x1000
0x101f4000 0x0010>;
};
...
}

## Slide 10: Memory Mapped Devices (External)
/ {
...
external-bus {
#address-cells = <2>
#size-cells = <1>;
ethernet@0,0 {
compatible = "smc,smc91c111";
reg = <0 0 0x1000>;
};
flash@1,0 {
compatible = "samsung,k8f1315ebm", "cfi-flash";
reg = <1 0 0x4000000>;
};
};
...
}

## Slide 11: Non Memory Mapped Devices
/ {
...
external-bus {
...
i2c@1,0 {
compatible = "acme,a1234-i2c-bus";
#address-cells = <1>;
#size-cells = <0>;
reg = <1 0 0x1000>;
rtc@58 {
compatible = "maxim,ds1338";
reg = <58>;
};
};
};
...
}

## Slide 12: How Interrupts Work
/ {
compatible = "acme,coyotes-revenge";
#address-cells = <1>;
#size-cells = <1>;
interrupt-parent = <&intc>;
serial@101f0000 {
compatible = "arm,pl011";
reg = <0x101f0000 0x1000>;
interrupts = < 1 0 >;
};
intc: interrupt-controller@10140000 {
compatible = "arm,pl190";
reg = <0x10140000 0x1000>;
interrupt-controller;
#interrupt-cells = <2>;
};
}

## Slide 13: Special Notes
aliases Note
  aliases {
  ethernet0 = &eth0; /* = /external-bus/ethernet@0,0 */
  serial0 = &serial0;
  };
chosen Note
  chosen { /* like boot arguments */
  bootargs = "root=/dev/nfs rw nfsroot=192.168.1.1 console=ttyS0,115200";
  };

## Slide 14: Typical Sequence of adding device tree support
Add device tree support to board files
  Start with a new dt-enabled board file
  Enable DT support in existing board files
Create a SoC specific and board specific device tree source files (dtsi and dts)
Enable DT support for system peripherals
  Interrupt Controller, GPIO, DMA
Enable DT support for peripheral drivers
  UART, I2C, SD/MMC, SPI, etc.

## Slide 15: Minimal Device Tree Enabled board file
static char const *exynos4210_dt_compat[] __initdata = {
"samsung,exynos4210",
NULL
};
DT_MACHINE_START(EXYNOS4210_DT, "Samsung Exynos4 (Flattened Device Tree)")
/* Maintainer: Thomas Abraham <thomas.abraham@linaro.org> */
.init_irq = exynos4_init_irq,
.map_io = exynos4210_dt_map_io,
.handle_irq = gic_handle_irq,
.init_machine = exynos4210_dt_machine_init,
.timer = &exynos4_timer,
.dt_compat = exynos4210_dt_compat,
.restart = exynos4_restart,
MACHINE_END
Note: http://lxr.linux.no/#linux+v3.3/arch/arm/mach-exynos/mach-exynos4-dt.c

## Slide 16: Minimal Device Tree Source file
/dts-v1/;
/ {
model = "Insignal Origen evaluation board based on Exynos4210";
compatible = "insignal,origen", "samsung,exynos4210";
memory {
reg = <0x40000000 0x40000000>;
};
chosen {
bootargs ="root=/dev/ram0 rw ramdisk=8192 initrd=0x41000000,8M console=ttySAC2,115200 init=/linuxrc";
};
}
Note: dtsi and dts files are located at arch/arm/boot/dts
http://lxr.linux.no/#linux+v3.3/arch/arm/boot/dts/exynos4210-smdkv310.dts

## Slide 17: Compiling (1)
Enable Device Tree Support
  menuconfig  boot options  flattened device tree
  Or use 'select USE_OF' in Kconfig entry of the device tree enabled board file
Build the kernel image
  make <defconfig>
  make menuconfig
  make uImage
  Builds the dtc compiler as well
    scripts/dtc
Build the device tree blob
  make <dts filename>

## Slide 18: Compiling (2)
Two options for passing dtb blob to kernel
  Use bootm command of u-boot
  Append dtb blob to the kernel image
Option 1: Using the bootm command
  Build u-boot with CONFIG_OF_LIBFDT enabled
  bootm <kernel base> <initrd base> <dtb base>
    Example: bootm 40007000 – 40004000
Option 2: Appending dtb blob to kernel
  menuconfig  boot options
    select “Use appended device tree blob”
  Used with legacy u-boot

## Slide 19: Instantiating platform devices from device tree - 1
Non-DT platforms relied on a static list of platform devices for all non-discoverable devices
For DT platforms, infrastructure exists to create platform devices at runtime from device tree
  of_platform_populate() call walks through the nodes in device tree and creates platform devices from it
    Call of_platform_populate during machine_init
  Nodes should have a compatible property
  For creating platform devices for sub-nodes, provide a list of all root nodes (second parameter)

## Slide 20: Instantiating platform devices from device tree - 2
static void __init exynos4210_dt_machine_init(void)
{
of_platform_populate(NULL, of_default_bus_match_table,
exynos4210_auxdata_lookup, NULL)
} Note: http://lxr.linux.no/#linux+v3.3/arch/arm/mach-exynos/mach-exynos4-dt.c
watchdog@10060000 {
compatible = “samsung,s3c2410-wdt”;
reg = <0x10060000 0x100>;
interrupts = <0 43 0>
};
rtc@10070000 {
compatible = “samsung,s3c2410-rtc”;
reg = <0x10070000 0x100>;
interrupts = <0 44 0>, <0 45 0>;
}
struct platform_device dt_watchdog = {
. . .
. . .
. . .
};
struct platform_device dt_rtc = {
. . .
. . .
. . .
};

## Slide 21: How to add minimal DT support for Device Drivers - 1
/dts-v1/;
/include/ "exynos4210.dtsi“
/ {
model = "Insignal Origen evaluation board based on Exynos4210";
compatible = "insignal,origen", "samsung,exynos4210";
memory {
reg = <0x40000000 0x40000000>;
};
chosen {
bootargs ="root=/dev/ram0 rw ramdisk=8192 initrd=0x41000000,8M console=ttySAC2,115200 init=/linuxrc";
};
watchdog@10060000 {
compatible = "samsung,s3c2410-wdt";
reg = <0x10060000 0x100>;
interrupts = <0 43 0>;
};
}

## Slide 22: How to add minimal DT support for Device Drivers - 2
static const struct of_device_id s3c2410_wdt_match[] = {
{ .compatible = "samsung,s3c2410-wdt" },
{},
};
MODULE_DEVICE_TABLE(of, s3c2410_wdt_match);
static struct platform_driver s3c2410wdt_driver = {
.driver = {
.owner = THIS_MODULE,
.name = "s3c2410-wdt",
.of_match_table = s3c2410_wdt_match,
.probe = s3c2410wdt_probe,
.remove = __devexit_p(s3c2410wdt_remove),
},
};
Note: http://lxr.linux.no/#linux+v3.3/drivers/watchdog/s3c2410_wdt.c

## Slide 23: Retrieving driver configuration data from device node - 1
Design the device tree node for the device that the driver will instantiate
  Compatible string
  Register base and memory region length
  IRQ numbers, if any
  Bindings for supplying platform/configuration data to the driver
  List of gpios if any
  Document the bindings in Documentation/devicetree/bindings/

## Slide 24: Retrieving driver configuration data from device node - 2
Modify the driver to obtain the data from the device node.
  Maintain a local copy of the platform data instead of referencing pdev->dev.pdata for pdata values
  Add a runtime check to determine if a device node is available.
    If node is available, parse all properties which the driver requires and populate the copy of local platform data
  Avoid parsing device node for properties after probe
    Keep a copy of the property value in private data

## Slide 25: Retrieving driver configuration data from device node - 3
Non-DT ARM platforms will continue to exist in few more kernel releases.
  Hence all DT support related additions should maintain compatibility to non-DT platforms.
Runtime determination of availability of a device tree node can be determined by checking of_node pointer
if (pdev->dev->of_node) {
/* DT based instantiation */
} else {
/* Non-DT based instantiation */
}

## Slide 26: Retrieving driver configuration data from device node - 4
i2c@13860000 {
compatible = "samsung,s3c2440-i2c";
reg = <0x13860000 0x100>
interrupts = <0 58 0>
samsung,i2c-sda-delay = <100>;
samsung,i2c-max-bus-freq = <20000>;
gpios = <&gpd1 0 2 3 0>,
<&gpd1 1 2 3 0>;
static void s3c24xx_i2c_parse_dt(struct device_node *np, struct s3c24xx_i2c *i2c)
{
struct s3c2410_platform_i2c *pdata = i2c->pdata;
if (!np)
return;
pdata->bus_num = -1;
of_property_read_u32(np, "samsung,i2c-sda-delay", &pdata->sda_delay);
of_property_read_u32(np, "samsung,i2c-slave-delay", &pdata->slave_delay);
of_property_read_u32(np, "samsung,i2c-max-bus-freq", (u32 *)&pdata->frequency);
}

## Slide 27: Setting up device names and platform data - 1
Platform devices instantiated from device tree are not assigned a device name
  Driver's looking up clocks would need device names
Device names can be assigned by
  Preparing a 'struct of_dev_auxdata' lookup table
  Passing that table to of_platform_populate()
Use the same 'struct of_dev_auxdata' lookup table to supply platform data, if required
Note: 'struct of_dev_auxdata' lookup table is a temporary solution

## Slide 28: Setting up device names and platform data - 2
serial@13800000 {
compatible = “samsung,exynos4210-uart";
reg = <0x13800000 0x100>
interrupts = <0 52 0>
};
serial@13800000 {
compatible = “samsung,exynos4210-uart";
reg = <0x13800000 0x100>
interrupts = <0 52 0>
};
static const struct of_dev_auxdata exynos4210_auxdata_lookup[] __initconst = {
OF_DEV_AUXDATA(“samsung,exynos4210-uart”,0x13800000,"exynos4210-uart.0“,NULL),
OF_DEV_AUXDATA(“samsung,exynos4210-uart”,0x13800000,"exynos4210-uart.1“,NULL),
{},
}
static void __init exynos4210_dt_machine_init(void)
{
of_platform_populate(NULL,of_default_bus_match_table,exynos4210_auxdata_lookup,NULL); }

## Slide 29: Callback functions in platform data of a driver
Determine if the callback functions can be dropped from platform data
  Implement callback functions in the driver
  Redesign the driver with no dependency on callbacks
In inevitable case, use the 'struct of_dev_auxdata' to pass the callback function pointers
  Populate only the callback function pointers in pdata
  Driver parses other pdata elements from DT
  But, this is just a temporary workaround since auxdata would be dropped eventually

## Slide 30: Guidelines for designing bindings
Should be OS agnostic
  Bindings should be reusable across all operating systems (and u-boot as well)
  If linux specific behavior needs encoding, use the 'linux' prefix for the binding.
Should be generic information which the driver can decode and program the hardware or setup the operating system
Should not be used to hard-code register values
  Acceptable in some cases for one-time writes
Should not be a used to encode read/modify/write cycles with information on delays.

## Slide 31: Supporting Platform
U-BOOT
  start from u-boot-1.3.0-rc1 (2007/9/7)
Kernel
  2.6.23
  2.6.34 (FDT)
  2.6.37 (PDT)

## Slide 32: Bootloader & Linux Support
U-BOOT
  bootm kernel_addr initrd_addr dtb_addr
Linux
  Kernel entry change
    old: kernel_entry(0, mach_id, atag_addr)
    new: kernel_entry(0, mach_id, dtb_addr)
  Config
    Boot option  Flattened Device Tree support
    Device Drivers  Device Tree and Open Firmware support  Support for device tree in /proc
  Device tree script
    arch/arm/boot/dts
  /proc/device-tree

## Slide 33: U-BOOT FDT Function
Get and keep FDT file address in RAM
Get FDT node
  const char *fdt_get_alias(const void *fdt, const char *name)
  int fdt_path_offset(const void *fdt, const char *path)
  int fdt_subnode_offset(const void *fdt, int parentoffset, const char *name)
Set FDT node
  int fdt_setprop_inplace(void *fdt, int nodeoffset, const char *name, const void *val, int len)
  static inline int fdt_setprop_inplace_cell(void *fdt, int nodeoffset, const char *name, uint32_t val)

## Slide 34: U-BOOT FDT Command
Usage:
fdt addr <addr> [<length>] - Set the fdt location to <addr>
fdt move <fdt> <newaddr> <length> - Copy the fdt to <addr> and make it active
fdt resize - Resize fdt to size + padding to 4k addr
fdt print <path> [<prop>] - Recursive print starting at <path>
fdt list <path> [<prop>] - Print one level starting at <path>
fdt set <path> <prop> [<val>] - Set <property> [to <val>]
fdt mknode <path> <node> - Create a new node after <path>
fdt rm <path> [<prop>] - Delete the node or <property>
fdt header - Display header info
fdt bootcpu <id> - Set boot cpuid
fdt memory <addr> <size> - Add/Update memory node
fdt rsvmem print - Show current mem reserves
fdt rsvmem add <addr> <size> - Add a mem reserve
fdt rsvmem delete <index> - Delete a mem reserves
fdt chosen [<start> <end>] - Add/update the /chosen branch in the tree
<start>/<end> - initrd start/end addr
NOTE: Dereference aliases by omiting the leading '/', e.g. fdt print ethernet0.
Example - http://www.denx.de/wiki/DULG/UBootCmdFDT

## Slide 35: Linux 3.0 ARM
setup_arch() (arch/arm/kernel/setup.c)
setup_machine_fdt() (arch/arm/kernel/devtree.c)
of_scan_flat_dt(early_init_dt_scan_chosen, boot_command_line)
of_scan_flat_dt(early_init_dt_scan_root, NULL)
of_scan_flat_dt(early_init_dt_scan_memory, NULL)

## Slide 36: Appendix